## Slide 1
Firearm Detection Using Wrist Worn Tri-Axis Accelerometer Signals
Md Abdullah Al Hafiz Khan, David Welsh, Nirmalya Roy
IEEE WristSense'18
March 19th, 2018

## Slide 2
Overview
  Introduction
  Motivation
  Related Work
  Methodology
  Data Collection
  Results and Discussion
  Limitations and Future Work

## Slide 3
Motivation
  Improve crime solving applications
  Acoustical 30 yard accuracy
  Expand sensor data use
  Assist in training
  Pervasive & non intrusive
  User specific adaptability
  Leverage existing sensors

## Slide 4
Related Work
Limited aspects of gunshots examined
  Acoustics, muzzle flash, bullet direction
  Handgun only recoil
Different sensor applications
  Limited wrist worn and smartphone
  Embedded in firearms
  Military base and city wide systems
Refinement of acoustic detection algorithms

## Slide 5
Sensing Paradigm
Custom devices exploit these distinguishable features
  Shot timers use sound and or recoil detection
  Military counter sniping detects muzzle flash and direction finding through sound
  City sensor networks locate sound point of origin
Limited and or expensive custom built sensors

## Slide 6
Solutions?
Smart Devices- Smartphone, Watch,
Available Sensors – Accelerometer, Gyroscope,
Microphone, etc.
Which sensor we use? - Accelerometer.
15 Firearm, Single shooter
Our comprehensive study –
Our Objectives –
Recognize Firearm, Firearm type, Firearm Category

## Slide 7
Different Firearms
15 firearms
Category
  Handgun
  Rifle
  Shotgun
Type
  Autoloading
  Manual
Firearm Details
Notes: Write the notes for the presenter

## Slide 8
Solutions
Firearms have different
  Shooting Style
  Hand positions
  Recoil force
Wristworn Accelerometer sensors
  Unique sensor signals for each firearm
Three shooting styles
Accelerometer Sensor Signals
Shooting Style
Notes: Write the notes for the presenter what are the shooting styles, how the sensor signals for different shooting style, specially note about the accelerometer sensor signals figures

## Slide 9: Our Framework
Preprocessing
  Create frames (1600 samples).
  Remove noise low-pass filter (150 Hz)
Frame Selection
    Gunshot related frames has Higher Energy (E > threshold)
Feature Extraction
  Statistical and frequency domain features
Firearm Category Selection
  Decision Tree Classifier
    Ease of implementation
    Realtime detection
Firearm Recognition
    Decision Tree (DT)
Firearm Type Detection
  1-class SVM
  Autoloaded samples as positive insntaces
  All others are negative instances
Frame Selection
Framework
Notes: Provide details for each of the module in the note so that presenter can present it nicely.

## Slide 10
Experimental Setup
Wristworn Sensors
  AX3 Watch, Axivity Ltd tri axis accelerometer
    Sampling frequency 1,600 Hz, offset +-16 G’s
    Dominant wrist of shoot
Participants
  Only one participant
  Height - 6'2'', Age 27, Weight - 180
Firearm shooting
    10 rounds for recoil under 10 ft/lbs
    5 rounds for recoil over 10 ft/lbs
Shooting Environments and Settings
  Private shooting range
  Flat level ground
  Target placed at torso height
  Target positioned 10 yards down range
  Shooter in standing position
Handgun
Rifle/Shotgun
Different types of Bullets
Shooting styles

## Slide 11: Evaluations
Firearm Category Inference
Three categories
    Handgun, Rifle, Shotgun
  Randomly split train and test set.
    training set contains 70% data
    Testing set contains 30% data
F1 scores for handgun 90%, rifle - 93%, shotgun 76%.
Different category has distinctive sensor signals.
Category Inference

## Slide 12: Evaluations
Firearm Detection
  Use Decision Tree to detect individual firearm
  Rifle detection
    'M44' and 'Scoped M91/30' have F1 score 60%, 58%.
    Both have similar impact on accelerometer sensor.
    Use same cartridge
    Both are non-autoloading
    Frame selection module selects non-gunshot related signals.
Ruger 10/22 has F1 score 93%
  Unique low recoil force
  Auto-loading
Rifle Inference Results

## Slide 13: Evaluations
Firearm Detection Comparison
  10-fold cross-validation
  Evaluated using DT, SVM, NB model.
F1 scores for rifle for DT, SVM, NB is 73%, 65%, 66% respectively
More number of rifle instances SVM performance dropped
Manual loading contains noises
Rifle Inference Comparison

## Slide 14: Evaluations
Firearm Type Detection
  Oneclass SVM
  Auoloading as positive instances
  Manual loading as negative instances
  Dataset was splitted randomly 70-30% as train and test
  Accuracy 90%
Firearm Type detection

## Slide 15
Limiatations
Sensor performance
  Sound level vs sound recording
Requires high sample rates
  Event length of 0.1 prevented data smoothing
  Overestimating accuracy
Training and testing samples
  Even vs uneven, 10 fold vs testing
Ambiguous conditions of shooting for HAR
  Walking and shooting sample

## Slide 16
Conclusions and Future work
  Firearm, type and category deteced
    Firearm detection accuracy
    Category Detection Accuracy
    Type detection accuracy
  Feature extraction
    Sliding-window spike detector
    Pre spike and post spike
  Multi-subjects investigations

## Slide 17
Thank you?
Sriram Chellappan
Associate Professor
University of South Florida
Dept. of Computer Science and Engineering
Email: sriramc@usf.edu
http://www.csee.usf.edu/~sriramc/